## Slide 1
R2R Dashboard Mathematical Workflow
Working equations, plant presets, excitation cases, simulation metrics, SysID estimates, and validation roadmap
Simulation: tension RMSE + overshoot
SysID: kt, kf, EA
Validation: logging, drift, retuning
Plants: P01-P10 EA presets
Future work
Dashboard mathematics, plant presets, excitation studies, and validation outputs
01

## Slide 2
How the Dashboard Works
R2R SysID Validation
1. Plant
P01-P10 preset
EA_N + metadata
baseline R/L/J/f/b
2. Excitation
ET1, ET3, ET6
E_Toggle, EVR
amplitude + noise
3. Controller
Outer tension PI
velocity PI
ZOH motor voltage
4. RK4 Model
1 ms physics
tensions + speeds
logged rows
5. Outputs
Simulation metrics
SysID estimates
validation plots
Simulation path
The selected plant changes the physical stiffness used in the state equations.
Excitation adds repeatable motor-voltage perturbations to the closed-loop controller output.
The simulator logs T1/T2/T3, omega_UW/omega_Nip/omega_RW, motor inputs, and velocities.
The result panel summarizes tension_rmse_N, max_overshoot_N, t90_s, control_effort_rms_V, samples, and duration.
SysID and validation path
Logged simulation rows become the regression data for parameter identification.
SysID estimates kt_UW, kt_Nip, kt_RW, kf_UW, kf_Nip, kf_RW, and EA.
Validation tabs compare logging rate, excitation profile, drift sensitivity, and retuning cost.
Calculation panels show one worked example so every output can be traced back to equations.
Dashboard mathematics, plant presets, excitation studies, and validation outputs
02

## Slide 3
Core State Equations Used by the Backend
R2R SysID Validation
State model
The equations tab now shows only equations that feed backend simulation, metrics, and SysID.
State and input vectors
x = [T1, T2, T3, omega_UW, omega_Nip, omega_RW]
u = [u_UW, u_Nip, u_RW]
v_i = R_i * omega_i
Web torque balance
tau_web,UW = (T3 - T1) * R_UW
tau_web,Nip = (T1 - T2) * R_Nip
tau_web,RW = (T2 - T3) * R_RW
Reduced three-span tension dynamics
dT1/dt = (EA/L1)(v_Nip - v_UW) - lambda_T(T1 - T1_ref)
dT2/dt = (EA/L2)(v_RW - v_Nip) - lambda_T(T2 - T2_ref)
dT3/dt = (EA/L3)(v_RW - 0.5(v_UW + v_Nip))
- lambda_T(T3 - T3_ref)
Roller velocity dynamics
domega_i/dt = (kt_i*u_i + tau_web,i - kf_i*omega_i) / J_i
J_i: roller inertia
kt_i: voltage-to-torque gain
kf_i: viscous friction
u_i: motor voltage command
These equations create the next state used for controller updates, metric calculations, and the logged rows that feed SysID.
Dashboard mathematics, plant presets, excitation studies, and validation outputs
03

## Slide 4
Controller, ZOH, and Time Scales
R2R SysID Validation
Outer tension PI correction
e_i = T_ref,i - T_i
c_i = Kp_star*e_i + (Kp_star/TI)*integral(e_i dt)
v_ref,UW = v_line - c1 - 0.5*c3
v_ref,Nip = v_line + c1 - c2 - 0.5*c3
v_ref,RW = v_line + c2 + c3
Velocity PI and feedforward
tau_cmd,i = Kvel*e_omega,i + (Kvel/TI_vel)*integral(e_omega,i dt) + tau_ff,i
tau_ff,i = kf_i*omega_ref,i - tau_web,i
u_i = clamp(tau_cmd,i / kt_i)
Every 1 ms
RK4
Fast physics step updates tension and roller speed.
Every 10 ms
PI
Controller computes a new motor-voltage command.
Between PI ticks
ZOH
Held input u stays constant while RK4 keeps integrating.
Every Tlog
PLC
Logged data becomes the source for SysID.
Example
If Ts = 10 ms and dt = 1 ms, one controller action contains 10 small physics calculations. Logging at Tlog = 20 ms records every second controller action, which directly affects SysID data density and accuracy.
Dashboard mathematics, plant presets, excitation studies, and validation outputs
04

## Slide 5
Plant Presets: What Changes Between P01-P10
R2R SysID Validation
Current dashboard behavior
Each plant uses supplement Table S12 EA_N and metadata.
Exact per-roller R, L, J, f, and b arrays are not yet supplied in the extracted JSON.
The backend therefore keeps baseline R/L/J/f/b until those arrays are available.
Dynamic safety policy
P01-P02 are inside the extracted baseline EA range. P03-P10 are high-EA cases; the app recommends zero excitation unless retuned inputs and exact arrays are supplied.
Why plant choice changes results
EA multiplies strain rate in dT/dt. A stiffer web converts the same speed mismatch into a larger tension-rate response.
Plant
Material / scale
EA_N
Regime
Recommended input
P01
PE / lab
3,200 N
O-UD
0.080 V
P02
PET / lab
9,600 N
O-UD
0.046 V
P03
PET / lab
40,000 N
H-Osc
0 V safety
P04
PET / pilot
50,000 N
O-UD
0 V safety
P05
Paper / prod
144,000 N
O-UD
0 V safety
P06
Al / lab
310,500 N
H-Damp
0 V safety
P07
Al / pilot
414,000 N
H-Osc
0 V safety
P08
Al / prod
1,242,000 N
O-UD
0 V safety
P09
Cu / lab
351,000 N
H-Damp
0 V safety
P10
Cu / pilot
351,000 N
O-UD
0 V safety
Validation meaning: plant comparisons are EA-driven until full per-roller arrays are added.
Dashboard mathematics, plant presets, excitation studies, and validation outputs
05

## Slide 6
Excitation Types: What Changes in the Inputs
R2R SysID Validation
Excitation
Type
Channels
Changing factors
ET1
single-channel sine
UW only
0.70 Hz sine on u_UW; u_Nip and u_RW are zero.
ET3
three-channel sine
UW, Nip, RW
0.55, 0.80, and 1.10 Hz sine waves with phase offsets.
ET6
three-channel multi-sine
UW, Nip, RW
Two sine components per motor input; richer frequency content than ET3.
E_Toggle
three-channel square/toggle
UW, Nip, RW
Square waves with staggered 0.42, 0.58, and 0.74 s periods.
EVR
event-varying random
UW, Nip, RW
Random held voltage values updated in 0.15 s buckets.
Why excitation changes the result
Excitation changes which motor channels move, how much frequency content reaches the system, and whether the logged data contains enough independent motion to identify kt, kf, and EA.
Dashboard behavior
Amplitude, tension noise, and omega noise alter the data quality. Larger amplitude improves excitation but can destabilize high-EA reduced-model runs; noise degrades SysID accuracy.
Equation tab
reference
Dashboard mathematics, plant presets, excitation studies, and validation outputs
06

## Slide 7
Simulation Outputs: Tension RMSE and Overshoot
R2R SysID Validation
Metrics calculated after each simulation run
tension_rmse_N = sqrt( sum((T_i[k] - Tref_i)^2) / (3N) )
max_overshoot_N = max_i,k( T_i[k] - Tref_i )
control_effort_rms_V = sqrt( sum(u_i[k]^2) / (3N) )
t90_s = first logged time all spans enter the settling band
Dashboard card
RMSE
Average tracking error across T1, T2, and T3.
Dashboard card
Overshoot
Largest positive tension excursion above target.
Workbook
XLSX
Summary sheet plus time-series data sheet.
How to read the simulation result
Plant changes EA_N and therefore the stiffness term inside dT/dt.
Excitation changes the voltage waveform added to u_UW, u_Nip, and u_RW.
The app logs each simulated state, calculates metrics, and writes the Excel summary for download.
Comparing plant/excitation pairs shows which inputs keep tension tracking stable.
Example report graph: plant-by-excitation tension RMSE comparison
Dashboard mathematics, plant presets, excitation studies, and validation outputs
07

## Slide 8
SysID Outputs: kt, kf, and EA
R2R SysID Validation
Motor parameter regression
J_i*domega_i/dt - tau_web,i = kt_i*u_i - kf_i*omega_i
Solve a two-parameter least-squares problem per roller:
[u_i, -omega_i] * [kt_i, kf_i]^T = J_i*domega_i/dt - tau_web,i
Outputs: kt_UW, kt_Nip, kt_RW, kf_UW, kf_Nip, kf_RW
Web stiffness regression
dT_i/dt + lambda_T(T_i - T_ref,i)
= EA * speed_strain_i / L_i
All spans share one least-squares estimate of EA.
Output: EA
Estimator output
ktension
Voltage-to-torque gain group reported as kt_* estimates.
Estimator output
kfriction
Viscous-friction group reported as kf_* estimates.
Estimator output
EA
Elastic modulus-area product estimated from tension dynamics.
Why excitation matters for SysID
A single channel can leave some parameters weakly observed.
Multi-channel/toggle/random inputs create richer independent motion.
Noise-free and sensor-noise cases should be validated separately.
Example report graph: SysID RMSE by plant and excitation
Dashboard mathematics, plant presets, excitation studies, and validation outputs
08

## Slide 9
Validation Types Covered by the Dashboard
R2R SysID Validation
Paper parts
Parameter extraction and paper-reference comparison for EA, R, L, J, f, and b.
Logging rate
Compares Tlog = 1-100 ms and checks how PLC data rate affects RMSE_theta.
Excitation
Compares ET1, ET3, ET6, E_Toggle, and EVR under noise-free and sensor-noise cases.
Drift
Compares EA drift, friction f drift, and reel inertia J drift sensitivity.
Retuning
Compares CS-BO(30), HGS-only, HGS+BO(5), and HGS+BO(10).
Retuning cost used in dashboard
cost = RMSE + 0.25*overshoot + 0.15*t90 + 0.015*control_effort
Validation question answered
Does the app reproduce the paper-style claim?
Which plant/excitation/logging/noise condition changes the result?
What calculation produced the displayed number?
All result tabs include worked calculations
Dashboard mathematics, plant presets, excitation studies, and validation outputs
09

## Slide 10
Future Work and Next Validation Steps
R2R SysID Validation
Noise validation
Run separate noise-free and sensor-noise validation sweeps.
Quantify how tension sensor noise and omega noise change RMSE_theta.
Add acceptance thresholds for each sensor-noise level.
Plant fidelity
Load exact per-plant R, L, J, f, and b arrays when available.
Retune excitation limits for P03-P10 high-EA plants.
Separate paper-reference validation from reduced-model safety policy.
Retuning extensions
Extend BO and HGS retuning from deterministic comparison to plant-specific optimization.
Track real-evaluation budget, final cost, and tension performance together.
Compare HGS+BO(5) with longer BO budgets across all plants.
Dashboard components to mature
Validation report generator: one-click PDF/DOCX/PPTX summaries from dashboard runs.
Plant/excitation comparison charts: heatmaps, grouped bars, and ranked tables.
Equation calculation examples: keep formulas synchronized with backend routes.
Research validation target
For every tab, state the paper claim, run the matching dashboard scenario, and report the numerical difference.
Document when a result is a full dynamic validation versus a safety-policy placeholder.
Keep outputs traceable: route, equation, input plant, excitation, noise, and metric.
Next milestone: validated noise-free/sensor-noise SysID report with BO/HGS retuning per plant
Dashboard mathematics, plant presets, excitation studies, and validation outputs
10